## Slide 1: IFTW WCS issue report flow
Traven

## Slide 2: Microsoft Dynamic365 – the issue system IFX use globally

## Slide 3: Registration – www.Infineon.com

## Slide 4: Case creation – Subject
[-oem-][-odm-][-project-][-obs-] short description
100 words as maximum
e.g.
  [HP][IEC][Hook2][OBS1234567] power button event lost
  [HP][TPV][Deora] PV1 power consumption too high

## Slide 5: Case creation – Description
Include these information and designate to Infineon FAE (email)
  Firmware / hardware version
  Expected behaviour
  Failure symptom
  Failure rate
  Reproduce steps
  Function recovery method
  Other necessary information

## Slide 6: Case creation – Collaboration
Customers can add collaborator themselves in the Portal for their colleagues or other non-Infineon people. If they need to add Infineon colleagues, they need to request via discussion board.

## Slide 7: Case creation – Attachment
Basic
  CC logs in CYPD4500 PD3.0 / PD2.0
  Ellisys C-Tracker logs
  SALEAE 6.25Mbps+ (digital), 1.625Mbps+ (analogue)
  LA files with toolchain name
  Others (test reports, screenshots or anything helpful to issues)
Recommended
  CC with SALEAE Pro at 1.2V digital (IFTW Logger)

## Slide 8: Case creation – Attachment format and file size
Upload limitation: 50MB
DO NOT overwrite if possible
Now allowed: ade;adp;app;asa;ashx;asmx;asp;bas;bat;cdx;cer;chm;class;cmd;com;config;cpl;crt;csh;dll;exe;fxp;hlp;hta;htr;htw;ida;idc;idq;inf;ins;isp;its;jar;js;jse;ksh;lnk;mad;maf;mag;mam;maq;mar;mas;mat;mau;mav;maw;mda;mdb;mde;mdt;mdw;mdz;msc;msh;msh1;msh1xml;msh2;msh2xml;mshxml;msi;msp;mst;ops;pcd;pif;prf;prg;printer;pst;reg;rem;scf;scr;sct;shb;shs;shtm;shtml;soap;stm;tmp;url;vb;vbe;vbs;vsmacros;vss;vst;vsw;ws;wsc;wsf;wsh.

## Slide 9: Case creation – Discussion board
The interaction section where there is exchange of information/comments between CRM users (Case owners, Collaborators) and portal users (Case creators). It provides options to add internal and external comments on the case.

## Slide 10: IFTW WCS Logger – helper for log collection

## Slide 11: SOP for log collecting – The WCS PD Host E2 training
 | INTEL Platform | AMD Platform | EVK Board | Checking Points
HW Signal | PCH_INT0# PCH_INT1# (Maple Ridge only) PCH_SDA PCH_SCL BBR_PWR BBR_RST SBU1/2 | APU_RST# APU_INT APU_SDA APU_SCL Retimer_SDA Retimer_SCL HPD SBU1/2 | MUX_SDA MUX_SCL HPD SBU1/2 | Is the I/O behavior normal !? Is the SBU signal normal !?
CC Log | CC Log | CC Log | CC Log | Is enter DP Alt mode? Is device issue the Attention HPD High message to Host?
I2C Log | PCH I2C Log Retimer I2C Log | APU I2C Log Retimer I2C Log | MUX I2C Log | Compare the PASS log and Fail log to dig out is anything abnormal.

## Slide 12: Infineon HOST PD Logger
Issue Information
Generic
  USB-C
  PD/PD to EC
AMD/INTEL Platform
  PD to APU/Ridge
  PD to MUX/Retimer
Start Recording
Pass Case
Fail Case

## Slide 13: Infineon HOST PD Logger – Function Flow
Launch Logger
Fill all data
Connect SALEAE pins accordingly
Hit
“Start Recording”
Do issue
replication steps
Save as Fail Case?
See issues?
Save as Pass Case?
Hit
“Abort Recording”
Hit
“Fail Case”
Hit
“Pass Case”
Finish?
Exit Logger
Yes
No
Yes
Yes
Yes
No
No
No

## Slide 14: Infineon HOST PD Logger – Prerequisites
A SALEAE 16ch/16ch Pro Logic Analyser.
Install SALEAE Logic2 (v2.4.0+) application.
Install “Manchester_PD_CC” CC analyser plugin (SALEAE Pro only).
Install “HPI_I2CBurst” I2C analyser plugin (Optional).

## Slide 15: Infineon HOST PD Logger – How to use (1/2)
Start Logger.
Fill all information and platform type in Version Information and mapping SALEAE pins with pre-defined channels or preferred ones.
    All fields are mandatory except “OEM Ticket#”.
    “Run” button will grey out if any blank field or channel duplicated.
Click “Start Recording” to start log collecting per setup.
Click “Abort Recording”, “Pass Case” or “Fail Case” while test finished.
Logger will assign relevant analysers to SALEAE logs and create a folder using current time format contains:
    Issue tracker form.
    SALEAE log files.
    Setup log: e.g. 20230522.txt

## Slide 16: Infineon HOST PD Logger – How to use (2/2)
Scenario A: SALEAE Logic is not running while starting Logger: (recommended)
    Will launch SALEAE Logic application with automation supportive automatically.
    Keep SALEAE Logic application running while log captures are finished.
    Will shutdown SALEAE Logic application while Logger is closed.
Scenario B: SALEAE Logic is running while starting Logger:
    Will use the running SALEAE Logic application, which needs to enable automation server before hand.
    Keep SALEAE Logic application running while log captures are finished.
    Will ***NOT*** shutdown SALEAE Logic application while Logger is closed.
Click “Start Recording” again for another capture cycle.
Close Logger while finish test.

## Slide 17: Logs submission
Zip all files and submit to case

## Slide 18: Infineon HOST PD Logger – Limitations
Logger might crash if PC doesn't install SALEAE Logic2 application.
Logger might crash if SALEAE Logic application doesn't enable "Automation Server" at Scenario B.
Doesn't support SALEAE Logic Analyser 8ch SKU.
DO NOT control SALEAE Logic application directly.
Logger cannot rename channel names in SALEAE log.

## Slide 19: We will …
Release firmware / documents on case instead of emails.
Turn down cases if insufficient information.
  Firmware / hardware version
  Expected behaviour
  Failure symptom
  Failure rate
  Reproduce steps
  Function recovery method
  Other necessary information
  Proper logs

## Slide 20: Questions?
LINE
traven.shih@infineon.com
ifx-traven